TOWN OF CORNWALL

Building Department

Building Official – Peter Russ

t. (860) 672-0711 c. (860) 480-9154

E-mail: bldginspection@cornwallct.gov

MINIMUM REQUIRED INSPECTIONS

Preliminary:  Prior to any work being started, site inspection at the request of the Building Official.

Electrical Service:  When CRS work order from Eversource is signed by the Electrician and turned in.

Footing:  After excavation and before footings are poured.

Foundation: After foundation is formed, but before it is poured.

Footing Drains: When pipe and stone are in place and filter fabric on site or in place.

Concrete Slab and Under Floor: Before slab is poured.

In Flood Hazard Area: Lowest floor elevation must be inspected including basement.

Framing: After roof sheathing and all framing, fire blocking and bracing are in place.

Plumbing Rough In: When rough work is completed and pipes are fire stopped at each level.

Electrical Rough In: When rough in work is completed and boxes made up.  All top bottom plate penetrations are to be fire stopped and required nail plates in place.

Mechanical/HVAC Rough In:  When rough work is completed. All duct work for the system shall have fire stopping at each floor level.

Fireplace and Masonry Chimney:  When steel is in place for hearths and before concrete is placed.  Also, at least once during smoke chamber and flue work.

Roofing Inspection: At time of installation of finish roof covering. (Minimum of 15 lb felt required under shingles.) Ice and water shield at eves 2’ into heated space.

Insulation:  After all insulation is in place and before covering with finish wall material.  R30 in floors, R30 in walls, R60 in ceilings or roof area.

Sheetrock or Plaster: After it is properly installed and before covering with tape or compound.

Fuel Tanks and Lines:  At the time of tank installation and when air test is on lines. (Includes LP gas.)

Other Inspections:  May be required at the discretion of the Building Official.

Final Inspection:  When all the work is completed, and all necessary signoffs from other agencies turned in we will issue a Certificate of Occupancy.

Office Hours:  Tuesday and Thursday, 7:00 AM to 9 AM and by appointment.